Lab Session 4
Meteorology and Climatology
Environmental Sciences Degree (Third Semester)
Prof. Francisco Pérez Bernal
2015-2016

---
Skew-T Log p Diagram Lab Session
Lab session where students are shown how to graphically apply the thermodynamical principles introduced in the subject for the study of meteorological parameters and atmospheric stability using the
Skew-T Log p Diagram (aka Herlofson Diagram)
[Speaker Notes: Es una representación gráfica conveniente de p, rho, T y m de forma que las procesos atmosféricos básicos sean representados de forma sencilla. Es una “fotografía” vertical del estado de la atmósfera.]

---
Lab Session Outline
Introduction
Atmospheric p and T lapse rates
Air parcel dynamics
Atmospheric stability
Skew-T Log p Diagram: basic concepts
Skew-T Log p Diagram: atmospheric quantities
Skew-T Log p: stability and levels of interest

---
Atmospheric Pressure Lapse Rate
size 24 {{dp'} over dz = - %rho' g_0}
size 24 {p' = %rho' r T'}
size 22{d ln(p' ) = -left (dz over H right)}
size 22{H = r {T'(z)} over g_0}
T' linear dependence
T' constant
size 21 {p' = p'_0 left({T'_0-%alpha z} over {T'_0}right)^{g_0 over{r %alpha} }}
size 21 {p' = p'_0 exp{left(-{g_0%DELTA z} over {r T'_0}right)} }

---
Environmental Lapse Rate (ELR)
size 20{T'=T'_0+{dT'}over{dz} %DELTA z + ...=T'_0-%alpha %DELTA z + ...}
Environmental Lapse Rate
size 25 {%alpha={-left({dT'}over{dz}right)}; %alpha = 6.5 nitalic { C lsup bold circ /km} }
ELR

---
Adiabatic Processes in the Atmosphere
Fast dynamics
Air low thermal conductivity
Convective motion in the atmosphere can be considered as ADIABATIC
This implies a decrease of temperature in the ascent of air parcels (adiabatic expansion) at the DALR Dry Adiabatic Lapse Rate.
Dry Adiabatic Lapse Rate
First Principle of Thermod.
size 22{%GAMMA = -left (dT over dz right ) = {g} over {c_p} }
Seudoadiabatic Processes
SATURATION
size 21 {%delta q = c_p dT- v dp}
Hydrostatics Fundamental Eq.
pf,Tf
size 20 {{dp'} over dz = - %rho' g_0}
Saturated
Air
pf,Tf
Dry Air
Useful approximations
size 21 {p = p'}
Mechanical Equilibrium
size 22{%GAMMA = 9.8 nitalic{C lsup{bold circ} /km}}
size 22{%GAMMA_s simeq 6.0 nitalic{C lsup{bold circ} /km}}
size 21 {T = T'}
Thermal Equilibrium
p0,T0
p0,T0

---
Atmospheric Stability (I)
Atmospheric Stability is determined by the temperature of the atmosphere around an ascending
air parcel. If the atmosphere is colder than the ascending parcel its density is larger and the
parcel keeps gaining height and viceversa.
size 20{T=T_0+{dT}over{dz} %DELTA z + ... = T_0 - %GAMMA %DELTA z + ...}
Stability consequences
Convective (vertical) air parcel motion is of the utter
importance for energy transfer in the atmosphere.
These motions are necessary for the occurrence of
precipitation .
size 20{T'=T'_0+{dT'}over{dz} %DELTA z + ...=T'_0-%alpha %DELTA z + ...}
size 22{a = {d^2 z} over {dt^2} = g left ({%rho^' - %rho} over {%rho} right ) =g left ({ T - T^'} over { T^'} right ) =g left ({%alpha-%GAMMA} over { T^'} right )%DELTA z }
size 30{a=-%eta %DELTA z }
size 30{%eta=g{%GAMMA-%alpha}over{T'}}
Stability Parameter

---
Atmospheric Stability (II)
Absolute Stability
size 30 {%alpha < %GAMMA_s < %GAMMA }
size 30 {%GAMMA_s < %alpha < %GAMMA }
size 30 { %GAMMA_s < %GAMMA < %alpha}
Absolute Instability
Adiabática seca
Adiabática saturada
Conditional Stability

---
Thermodynamic Diagrams: Definition
Thermodynamic Diagrams: Diagrams where pressure, density, temperature,
Mixing ratio and other parameters are depicted in such a way that state equations.
the first principle of Thermodynamics, and Clausius-Clapeyron equation are
Satisfied in adiabatic and seudoadiabatic processes.
Source: Glossary of Meteorology, American Meteorological Society

---
Skew-T Log p – Lines of interest
Isobars
Isotherms
Dry Adiabatic
Saturated Moist
Adiabatic
Saturation Mixing Ratio
[Speaker Notes: (a) Casi todas las isopletas de interés son aprox. rectas. (b) El ángulo entre adiabáticas e isotermas permite trabajar gráficamente con comodidad. (c) El área en el diagrama es proporcional al trabajo puesto en juego. (d) La altura en la atmósfera es aproximadamente la coordenada vertical del diagrama. (e) En el diagrama normalizado se puede observar toda la troposfera, hasta la estratosfera. Aprox. Burbuja y Seudoadiabática --> no confundir con otro diagrama.]

---
Skew-T Log p: Atmospheric Soundings
Temperature soundigs are carried out every 6 or 12 hours, always at 00.00 UTC and
at 12.00 UTC, in approx 800 locations around the world.
These soundings make use of radiosondes, dropsondes, soundings with airplanes or
rockets and pibals or rawinsondes.
Data received ...
… and decoded
08495 LXGB Gibraltar Observations at 00Z 06 Mar 2009
  PRES HGHT TEMP DWPT RELH MIXR DRCT SKNT THTA THTE THTV
    hPa m C C % g/kg deg knot K K K
----------------------------------------------------------------------------
 1015 4 13.6 6.6 63 6.06 270 19 285.5 302.7 286.6
 1000 134 12.4 6.4 67 6.06 285 24 285.6 302.7 286.6
   900 1005 4.6 2.2 84 5.01 294 38 286.2 300.6 287.1
  850 1469 2.2 -4.8 60 3.16 290 32 288.4 297.8 289.0
  824 1721 4.2 -20.8 14 0.89 320 34 293.1 296.0 293.3
  801 1951 5.2 -19.8 14 1.00 335 42 296.6 299.9 296.8
  700 3038 -1.3 -15.3 34 1.67 325 56 301.0 306.4 301.3
  649 3635 -5.9 -15.3 47 1.80 320 52 302.3 308.2 302.7
  597 4286 -9.8 -18.7 48 1.47 315 64 305.2 310.0 305.4
  552 4890 -11.9 -27.9 25 0.70 325 65 309.6 312.1 309.7
  500 5640 -17.9 -31.9 28 0.53 335 69 311.1 313.1 311.2
  400 7270 -27.9 -40.9 28 0.27 325 80 318.6 319.7 318.7
  300 9270 -44.7 -52.7 40 0.10 335 90 322.2 322.6 322.3
  200 11860 -64.1 -68.0 59 0.02 335 112 331.1 331.2 331.1
  100 16130 -63.9 -89.9 2 0.00 295 58 404.0 404.0 404.0
 TTAA 56001 08495 99015 13657 27019 00134 12456 28524 92780 06423 29033 85469
02257 29032 70038 01364 32556 50564 17964 33569 40727 27963 32580 30927 44758
33590 25046 54343 34104 20186 64139 33612 15362 60971 32078 10613 63976 29558
88203 64339 33609 77231 34117 41710 31313 48008 82331
 TTBB 56008 08495 00015 13657 11015 13457 22971 10249 33921 06222 44900 04624
55857 01010 66849 02659 77842 03866 88831 04675 99824 04275 11801 05275 22785
04466 33693 01764 44672 04161 55616 08757 66559 12163 77552 11966 88514 16365
99478 20762 11453 22366 22446 22166 33430 23968 44388 ..........................................
More info:
Atmospheric Sounding Data: Datos de sondeos en altura. Departamento de CC Atmosféricas de la U. Wyoming
Federal Meteorological Handbook #3 Rawinsonde and Pibal Observations FCM-H3-1997
[Speaker Notes: Rawinsonde Radiosonde which is tracked by radar or radio-theodolite to measure the wind aloft. radiosondes are deployed by being dropped from an aircraft instead of being carried aloft by a balloon. Radiosondes deployed in this way are called dropsondes. They are most often used in special research projects, such as when it is desired to obtain a profile through a specific feature of a storm. Tres sondeos como máximo simultáneamente. Permiten evaluar que evolución sigue la atmósfera.]

---
Skew-T Log p: Atmospheric Parameters
  PRES TEMP DWPT
    hPa ºC ºC
----------------------------
 1015.0 13.6 6.6
 1000.0 12.4 6.4
  900.0 4.6 2.2
  850.0 2.2 -4.8
  800.0 3.0 -19.8
  700.0 -1.3 -15.3
  650.0 -5.9 -15.3
  600.0 -9.8 -18.7
  550.0 -11.9 -27.9
  500.0 -17.9 -31.9
  400.0 -27.9 -40.9
  300.0 -44.7 -52.7
  200.0 -64.1 -68.0
  100.0 -63.9 -89.9
[Speaker Notes: Ayuda a determinar la altura de la base y la cima de las nubes, de acuerdo con la saturación. Cuando T es aprox. igual a Tr el aire está saturado y existe condensación. La base viene determinada por una brusca disminución de T-Tr y la cima por el descenso de Tr.]

---
Atmospheric Parameters
Mixing Ratio
smr at dewpoint temperature
m(850hPa) = 3.2 g/kg
Saturation Mixing Ratio
smr at atmospheric temperature
M(850hPa) = 5.1 g/kg

---
Atmospheric Parameters
Relative Humidity:
Method (I)
size 22 {h simeq 100 {m} over {M} = 100 3.2 over 5.1 = 63"%"}
h = 620/10 =62%
Relative Humidity:
Method (II)
(1) Starting from the Td of the pressure level under study we draw a trajectory parallel to smr to the 1000 mb level.
(2) We draw from this point a line
parallel to isotherms.
(3) From the T of the level under study a straight line is drawn, parallel to smr lines, until it intersects item (2) line.
(4) The pressure marked by this point divided by 10 is the relative humidity.

---
Atmospheric Parameters
Vapor Tension (e):
(1) Starting from the dewpoint temperature Td, a straight line parallel to the isotherms is drawn to the pressure level 622 hPa.
622 hPa
(2) The smr marked in this point is the vapor tension in hPa of the level under study.
(3) The saturation vapor pressure (E) is computed in the same way but starting from the T of the level under study.
e = 4.1 hPa
Virtual Temperature:
(1) The difference Tv-T is approx. equal to 1/6 of the smr at the dewpoint temperature Td.
Tv - T = 3.2/6 ≈ 0.5ºC

---
Atmospheric Parameters
Potential Temperature (θ):
θ = 288 K
(1) Starting from the T of the level under study, a trajectory paralled to the dry adiabaths is drawn to the pressure level of 1000 hPa.
(2) The temperature in this point of intersection is the potential temperature
Equivalent Temperature:
(1) Starting from the Td of the level under study, draw a trajectory parallel to the smr lines.
(2) Starting from the T of the level under study, draw a line paralel to the dry adiabaths until it intersects the previous line.
(3) From this point draw a line parallel to the saturated adiabaths until the moist and dry adiabaths coincide.
(4) Turn back to the level under study following the dry adiabaths. The temperature marked is the equivalent temperature Teq.
Teq = 12ºC

---
Skew-T Log p Diagram: Stability Study
Every layer where the ELR is approximatedly linear is studied:
A layer is absolutely stable if the ELR is less than the SALR (Saturated Adiabatic Lapse Rate)
A layer is absolutely unstable if the ELR is larger than the DALR (Dry Adiabatic Lapse Rate).
A layer is conditionally unstable if the ELR is between the SALR and the DALR.
A.U.
A.S.
C.U.
[Speaker Notes: Amanecer/Anochecer favorece la inestabilidad/estabilidad. Una atmósfera inestable está bien mezclada. El pico de mezcla se alcanza pasado el mediodía y la atmósfera se homogeneiza. En estos casos en el diagrama : La razón de mezcla (Tr sigue la curva de rs) y la temperatura potencial (T sigue la curva de T) se hacen constantes con la altura.]

---
Levels of Interest
LCL:
Lifting Condensation Level
(1) Starting from Td of the level under study, draw a trajectory parallel to the lines of constant smr.
LCL850 =2300 m
(2) From T of the level under study, draw a line parallel to the dry adiabats, the intersection with the previous line is the LCL.
CCL:
Convective Condensation Level
(1) From surface Td draw a line parallel to the smr lines.
(2) The intersection of this line with the ELR is the CCL.
CCL =1050 m
(3) From the CCL draw a line parallel to the dry adiabats. The surface temperature marked by this line is the convection temperature (CT).
CT = 17ºC
[Speaker Notes: NCA: Nivel en el que condensará una masa que ascienda de forma adiabática desde determinado nivel (p.e. ascenso frontal, en zona de baja presión no térmica u orográfico). Base de nubes (estratiformes) formados por ascenso en estos casos. NCC: Nivel donde comienza la condensación de una masa de aire que se eleva calentada desde la superficie hasta la TCD. Base de nubes convectivas.]

---
Levels of Interest
LFC:
Level of Free Convection
Remember that the existance of the LFC,
and the equilibrium levels ELm and ELc
Depends on the shape of the existing ELR.
(1) From the LCL draw a line parallel to moist adiabats until intersecting the ELR.
Attention. This level does not always exist.
ELm:
Mechanical Lifting Equilibrium Level
(1) From the LFC draw a line parallel to the saturated adiabats. The intersection of this line with the ELR is the ELm.
Attention. This level does not always exist.
ELm
ELc
ELc:
Convective Lifting Equilibrium Level
CCL
LFC
(1) From the CCL draw a line parallel to the saturation adiabats. The intersection of this line with the ELR is the ELm.
Attention. This level does not always exist.
LCL
[Speaker Notes: NCL: El nivel en el que una burbuja que se eleva adiabáticamente hasta su saturación y prosigue siguiendo la adiabática saturada llega a estar a mayor temperatura que la atmósfera que la rodea. El movimiento vertical prosigue hasta que llega a la altura de equilibrio (NEM) donde se igualan la temperatura de la burbuja y la de la atmósfera.]

---
Positive and Negative Areas
Mechanical Lifting
From the LCL draw a line upwards parallel to the closest saturation adiabat and downwards parallel to the closest dry adiabat.
Those areas where the ELR is to the right of the previous line convey negative potential energy, while those areas where the ELR is to the left have positive potential energy (CAPE).
(CAPE: Convective Available Potential Energy)
[Speaker Notes: Otros aspectos de interés: Cálculo de espesores. Representación e influencia del viento. Índices de interés.]

---
Positive and Negative Areas
Convective Lifting
From the CCL draw a line upwards parallel to the closest saturation adiabat, and downwards following the closest dry adiabat.
Those areas where the ELR is to the right of this line convey negative potential energy, while those to the left have positive potential energy.
[Speaker Notes: Una burbuja que se eleve y alcance un áreas positiva continúa su ascenso libremente y son regiones inestables donde pueden formarse nubes con una gran extensión vertical.]

---
Bibliography
Skew-T Log-p Diagram Analysis Procedures.
 Air Weather Service Technical Report TR-79/006.
Atmospheric Sciences 301, University of Washington. SKEW-T, LOG-P DIAGRAM ANALYSIS PROCEDURES;
http://www.atmos.washington.edu/~houze/301/Miscellaneous/Skew-T.pdf
Murry L. Salby, Fundamentals of Atmospheric Physics;
Associated Press 1996.
Walter J. Saucier, Principles of Meteorological Analysis;
Dover Publications, INC. 1989.